## Slide 1: MDO – Marketing Digital Outdoor
Embedded Systems
Design
José Pires | A50178
Hugo Freitas | A88258
Group 8:

## Slide 2: Agenda
Recap
  Problem statement
  Analysis – System Overview
Theoretical Foundations
Design
  HW
  SW

## Slide 3
1. Introduction

## Slide 4: Problem Statement
The project consists of a marketing digital outdoor (MDO) with:
  sound and video display, and fragrance emission selected by the brands,
  providing a gesture-based interface for user interaction to create pictures and GIFs, brand-specific,
  and share them on social media.

## Slide 5: Analysis System Overview

## Slide 6: Analysis System Overview
Hardware Architecture

## Slide 7: Analysis System Overview
Software Architecture
  Remote Client

## Slide 8: Analysis System Overview
Software Architecture
  Remote Server

## Slide 9: Analysis System Overview
Software Architecture – Local System

## Slide 10
2. Theoretical Foundations

## Slide 11: Theoretical Foundations Scenting Technologies
These are all the topics that are addressed in this project:
  Project Methodology;
  Concurrency;
  Threads versus processes;
  Communications;
  Daemons;
  Device Drivers;
  Build systems and Makefiles;
  Source code documentation;

## Slide 12: Theoretical Foundations Scenting Technologies
These are all the topics that are addressed in this project:
  Scenting Technologies;
  Computer Vision;
  RDBMS;
  Motion Detection;
  Camera Recording and codecs;
  Image filtering;
  GIF Generation;
  Social Media APIs
  UI Framework
  File transfer Protocols

## Slide 13: Theoretical Foundations Scenting Technologies
A scenting technology transforms an aromatic liquid into a gaseous fluid that can be conveyed through the air and be captured by human olfactory sense, usually for therapeutic or marketing purposes.
Types:
  Thermalization
    Heat source to induce evaporation
    Causes adulteration of the fragrance
    Energy intensive process
  Evaporation
    Natural evaporation of the chemicals
    Too slow
  Atomization
    Ultrasonic:
      use water
      Simpler
      cheaper
    Nebulizers:
      don’t use water
      Don’t cause adulteration of the fragrance
      More expensive and more costly

## Slide 14: Theoretical Foundations Scenting Technologies
Ultrasonic Diffusion:
  high frequency stimuli (>20 kHz) to brake down water molecules into droplets, producing mist, diffusing the oils into the air.
  Accomplished using micro-mesh piezoelectric transducers.

## Slide 15: Theoretical Foundations Scenting Technologies
Ultrasonic Diffusion:
  high frequency stimuli (>20 kHz) to brake down water molecules into droplets, producing mist, diffusing the oils into the air.
  Accomplished using micro-mesh piezoelectric transducers.

## Slide 16: Theoretical Foundations Computer Vision
Transformation of data from a still image or video camera into either a decision or a new representation to achieve some particular goal [36].
Computer vision framework
  OpenCV: it is an open-source computer vision and machine learning software library, built to provide a common infrastructure for computer vision applications and accelerate the use of machine perception in commercial products.
Face detection
  Recent studies [47, 48] show that face detection can be further improved by using deep learning, leveraging the high capacity of deep convolutional networks.

## Slide 17: Theoretical Foundations Computer Vision
Haar Cascade classifier

## Slide 18: Theoretical Foundations Computer Vision
Haar Cascade classifier

## Slide 19: Theoretical Foundations Computer Vision
Hand Gesture Recognition

## Slide 20: Theoretical Foundations Computer Vision
Hand Gesture Recognition

## Slide 21: Theoretical Foundations RDBMS
Levels of abstraction

## Slide 22: Theoretical Foundations RDBMS
Structure

## Slide 23: Theoretical Foundations RDBMS
Database Design: Entity-Relation Diagram (ERD)

## Slide 24: Theoretical Foundations RDBMS
RDBMS selection:
  Oracle Database: proprietary
  Microsoft SQL Server: proprietary
  MySQL:
    Open-source
    Scalable
    Client-server architecture
    User authentication & Security features
  SQLite
    Open-source
    File-based (not scalable)
    Lacks user authentication & Security features

## Slide 25: Theoretical Foundations RDBMS
Structured Query Language (SQL):
  Data Definition Language (DDL)
  Data Manipulation Language (DML)

## Slide 26: Theoretical Foundations RDBMS
SQL: Data Definition Language (DDL)

## Slide 27: Theoretical Foundations RDBMS
SQL: Data Manipulation Language (DML)

## Slide 28: Theoretical Foundations RDBMS
MySQL C++ connector:

## Slide 29: Theoretical Foundations Motion Detection
The MDO-L needs to be capable of detecting a user, in order to switch between normal mode to interaction mode.
Ultrasonic Sensor
  The sensor determines the distance to a target by measuring time lapses between the sending and receiving of the ultrasonic pulse [69].

## Slide 30: Theoretical Foundations Camera recording and codecs
Video encoding formats, also called video file formats, are methods of optimizing digital video files for different platforms, programs, and devices.
Processes of video encoding:
  Compression: decreases the size of a video file so that it is more manageable. Without proper compression, most files would be far too large to upload easily, load quickly, or play smoothly on users’ devices.
  Transcoding: refers to the total audio and video conversion process from one video format to another. It ensures that a video file is compatible with the video player and/or platform it is using. Without transcoding, users would not be able to watch the video file at all.

## Slide 31: Theoretical Foundations Image Filtering
After detect the face, it is now possible to apply filters like this figure.
Scaling the image having in touch the face size and put the image in front of the face.

## Slide 32: Theoretical Foundations GIF Generation
The main features of GIF are:
  Up to 256 colors using 1 to 8 bits per pixel
  Multiple images per file: supporting animation.
APIs
  MagickWand — C [78]: recommended interface between the C programming language and the ImageMagick image processing libraries.
  MagickCore — C [79]: low-level interface between the C programming language and the ImageMagick image processing libraries. Recommended for power users.
  Magick++ — C++ [80]: object-oriented C++ API to the ImageMagick image-processing library.
    It supports manipulation and conversion of OpenCV data structures — which are used to store frames from the camera and to process them — thus making it the chosen solution.

## Slide 33: Theoretical Foundations Social Media Sharing APIs
These platforms expose a set of features through APIs to external agents interact with them in a programmatic way, enabling automation of tasks like content sharing, scheduling, search, etc.
Twitter: less complex API from all SMs

## Slide 34: Theoretical Foundations Social Media Sharing APIs
Twitter API: To interact with the Twitter platform, one can make a request and retrieve its response by following these steps [87]:
  Select the end-point;
  Select a tool to make the request;
  Review the response;
  Adjust the request using parameters.

## Slide 35: Theoretical Foundations UI Framework
QT was the chosen one for the following reasons:
  Allows cross development;
  Cost: open-source license (free) and faster to implement
  Implementation: implemented in C++, which means that it is possible to use many libraries.

## Slide 36: Theoretical Foundations File Transfer Protocols
HTTPS:
  The communications between subsystems are made through TCP/IP, this is also used in this protocol which is an advantage;
  The data is transferred only with authentications (request and responses) which makes it more secure;
  All communication is encrypted, which makes it even more secure.
Third Party API:
  Transfer.sh: This application has easy-to-use commands in order to transfer files with a URL, there is unlimited upload, it can encrypt files and it is also possible to limit the amount of downloads and days available of downloading [104].
  Curlpp: Using the library curlpp with the transfer.sh API, it is possible to create a program to transfer files between nodes automatically when requested from the user

## Slide 37
3. Design

## Slide 38
3.1. Hardware

## Slide 39: Design Hardware Architecture

## Slide 40: Design Hardware Architecture
Main Controller:
  Processor: Broadcom BCM2711 processor, quad-core Cortex-A72 (ARM v8) 64-bit with 1.5GHz;
  Memory: 4GB LPDDR4 with on-die ECC;
  Connectivity: 2.4 GHz and 5.0 GHz IEEE 802.11b/g/n/ac wireless LAN, Bluetooth 5.0 with low energy, one Gigabit Ethernet port, four USB ports in which two are 3.0 and another two are 2.0;
  GPIO: standard 40-pin GPIO fully backwards-compatible with previous boards;
  Video and Sound: two HDMI ports that support up to 4kp60, a 2-lane MIPI DSI display port, a 2-lane MIPI CSI camera port and a 4-pole stereo audio and composite video port;
  Multimedia: H.265 (4Kp60 decode), H.264(1080p60 decode and 1080p30 encode) and OpenGL ES 3.0 graphics;
  SD card support: Micro SD card slot for loading operating system and data storage;
  Input power: 5V Direct Current (DC) via USB-C connector (minimum 3A), 5V DC via GPIO header (minimum 3A) and Power over Ethernet (PoE) - enabled (requires separate PoE HAT);
  Environment: it has a range of operation between 0ºC and 50ºC.

## Slide 41: Design Hardware Architecture
Motion Detection(HC-SR04):
  Operating Voltage: 5V DC;
  Operating Current: 15 milliampere (mA);
  Operating Frequency: 40 KHz;
  Maximum Range: 4 meters;
  Minimum Range: 2 centimeters;
  Ranging Accuracy: 3 millimeters;
  Measuring Angle: 15 degrees;
  Trigger Input Signal: 10 microseconds TTL pulse;
  Dimension: 45 x 20 x 15 millimeters.

## Slide 42: Design Hardware Architecture
Fragrance diffusion actuator:
  Operating Voltage: 5V DC;
  Operating Current: 300 milliampere (mA);
  Operating Power: 2 W;
  Operating Frequency: 108 kHz;
  Dimension: 35 x 20 x 17 millimeters.

## Slide 43: Design Hardware Architecture
Camera (Raspberry Pi Camera Module V2):
  Sensor: Sony IMX219 8-megapixel;
  Quality: 1080p30, 720p60;
  Interface: CSI;

## Slide 44: Design Hardware Architecture
LCD Display:

## Slide 45: Design Hardware Architecture
Speakers (Raspberry Pi Camera Module V2):
  Impedance: 8 Ohm;
  Power: 5 W;
  Interface: JST PH2.0.

## Slide 46: Design Hardware Architecture
Power Supply:
  Output: 4 USB-A 2.4 A ports.

## Slide 47: Design Hardware Architecture
Total cost:

## Slide 48: Design Hardware Interfaces Definition

## Slide 49: Design Hardware Interfaces Definition

## Slide 50: Design PCB Design
Schematic

## Slide 51: Design PCB Design
Layout

## Slide 52: Design Hardware Test Cases

## Slide 53: Design Hardware Tools
PADS
  Logic
  Layout

## Slide 54
3.2. Software

## Slide 55: Design Component Diagram
Remote Client

## Slide 56: Design Component Diagram
Remote Server

## Slide 57: Design Component Diagram
Remote Server (1/2)

## Slide 58: Design Component Diagram
Remote Server (2/2)

## Slide 59: Design Component Diagram
Local System

## Slide 60: Design Component Diagram
Local System (1/3)

## Slide 61: Design Component Diagram
Local System (2/3)

## Slide 62: Design Component Diagram
Local System (3/3)

## Slide 63: Design Deployment Diagram

## Slide 64: Design Class Diagram
Remote Client

## Slide 65: Design Class Diagram
Remote Client (1/4)

## Slide 66: Design Class Diagram
Remote Client (2/4)

## Slide 67: Design Class Diagram
Remote Client (3/4)

## Slide 68: Design Class Diagram
Remote Client (4/4)

## Slide 69: Design Class Diagram
Remote Server

## Slide 70: Design Class Diagram
Remote Server (1/4)

## Slide 71: Design Class Diagram
Remote Server (2/4)

## Slide 72: Design Class Diagram
Remote Server (3/4)

## Slide 73: Design Class Diagram
Remote Server (4/4)

## Slide 74: Design Class Diagram
Local System (1)

## Slide 75: Design Class Diagram
Local System (1): 1/3

## Slide 76: Design Class Diagram
Local System (1): 2/3

## Slide 77: Design Class Diagram
Local System (1): 3/3

## Slide 78: Design Class Diagram
Local System (2)

## Slide 79: Design GUI Layouts
Remote Client

## Slide 80: Design GUI Layouts
Remote Client (1/2)

## Slide 81: Design GUI Layouts
Remote Client (2/2)

## Slide 82: Design GUI Layouts
Remote Server

## Slide 83: Design GUI Layouts
Local System

## Slide 84: Design GUI Layouts
Local System (1/2)

## Slide 85: Design GUI Layouts
Local System (2/2)

## Slide 86: Design Software Test Cases
Remote Client

## Slide 87: Design Software Test Cases
Remote Server

## Slide 88: Design Software Test Cases
Local System

## Slide 89: Design Software Test Cases
Local System

## Slide 90: Design Class Topics mapping (Local System)
Device drivers & Daemons:
Pthreads: multithreading
TCP/IP: client-server architecture between LS and RS
Task synchronization:
  Mutexes
  Condition variables
  Semaphores

## Slide 91: Design Third-party libraries & APIs
Local System
  OpenCV: computer vision
  Magick++: GIF generation
  MySQL: DB management
  Twitter REST APIs
  Curlpp + Transfer.sh: file transfer
  Qt: UI framework

## Slide 92: Design Software Tools
Plantuml: draw UML diagrams
Make: and makefiles
Doxygen: source-code documentation
Qt: UI Framework
Buildroot
Linux

## Slide 93: References

## Slide 94: References

## Slide 95: References

## Slide 96: References

## Slide 97: References

## Slide 98: References

## Slide 99: References

## Slide 100: References