## Slide 1: MDO – Marketing Digital Outdoor
Embedded Systems
Design
José Pires | A50178
Hugo Freitas | A88258
Group 8:

## Slide 2: Agenda
Recap
  Problem statement
  Analysis – System Overview
Theoretical Foundations
Design
  Hardware Specification
  Hardware Interfaces Definition
  Software Specification
  Software Interfaces Definition

## Slide 3
1. Introduction

## Slide 4: Problem Statement
The project consists of a marketing digital outdoor (MDO) with:
  sound and video display, and fragrance emission selected by the brands,
  providing a gesture-based interface for user interaction to create pictures and GIFs, brand-specific,
  and share them on social media.

## Slide 5: Analysis System Overview

## Slide 6: Analysis System Overview
Hardware Architecture

## Slide 7: Analysis System Overview
Software Architecture
  Remote Client

## Slide 8: Analysis System Overview
Software Architecture
  Remote Server

## Slide 9: Analysis System Overview
Software Architecture – Local System

## Slide 10
2. Theoretical Foundations

## Slide 11: Theoretical Foundations Scenting Technologies
These are all the topics that are aborded in this project:
  Project Methodology;
  Concurrency;
  Threads versus processes;
  Communications;
  Daemons;
  Device Drivers;
  Build systems and Makefiles;
  Source code documentation;
  Scenting Technologies;
  Computer Vision;
  RDBMS;
  Motion Detection;
  Camera Recording and codecs;
  Image filtering;
  GIF Generation;
  C/C++ Libraries and APIs;
  Social Media APIs
  UI Framework
  File transfer Protocols

## Slide 12: Theoretical Foundations Scenting Technologies
A scenting technology transforms an aromatic liquid into a gaseous fluid that can be conveyed through the air and be captured by human olfactory sense, usually for therapeutic or marketing purposes.
Ultrasonic Diffusion:
  Ultrasonic diffusion uses high frequency stimuli to brake down water molecules into droplets, producing mist, diffusing the oils into the air. The high frequency stimuli is above 20 kHz, the upper threshold for audible human hearing — thus the ultrasonic naming — and it’s accomplished using micro-mesh piezoelectric transducers.

## Slide 13
Theoretical Foundations Scenting Technologies

## Slide 14
Theoretical Foundations Scenting Technologies

## Slide 15: Theoretical Foundations Computer Vision
Computer vision is a vast field, but can broadly be defined as the transformation of data from a still image or video camera into either a decision or a new representation to achieve some particular goal [36].
Computer vision framework
  OpenCV: it is an open-source computer vision and machine learning software library, built to provide a common infrastructure for computer vision applications and accelerate the use of machine perception in commercial products.
Face detection
  Recent studies [47, 48] show that face detection can be further improved by using deep learning, leveraging the high capacity of deep convolutional networks.

## Slide 16: Theoretical Foundations Computer Vision
Haar Cascade classifier

## Slide 17: Theoretical Foundations Computer Vision
Haar Cascade classifier

## Slide 18: Theoretical Foundations Computer Vision
Hand Gesture Recognition

## Slide 19: Theoretical Foundations Computer Vision
Hand Gesture Recognition

## Slide 20: Theoretical Foundations RDBMS
Levels of abstraction

## Slide 21: Theoretical Foundations RDBMS
Structure of a RDBMS

## Slide 22: Theoretical Foundations RDBMS
Example of na ERD

## Slide 23: Theoretical Foundations RDBMS
SQL

## Slide 24: Theoretical Foundations RDBMS
SQL

## Slide 25: Theoretical Foundations RDBMS
SQL

## Slide 26: Theoretical Foundations Motion Detection
The MDO-L needs to be capable of detecting a user, in order to switch between normal mode to interaction mode.
Ultrasonic Sensor
  The sensor determines the distance to a target by measuring time lapses between the sending and receiving of the ultrasonic pulse [69].

## Slide 27: Theoretical Foundations Camera recording and codecs
Video encoding formats, also called video file formats, are methods of optimizing digital video files for different platforms, programs, and devices.
Processes of video encoding:
  Compression: decreases the size of a video file so that it is more manageable. Without proper compression, most files would be far too large to upload easily, load quickly, or play smoothly on users’ devices.
  Transcoding: refers to the total audio and video conversion process from one video format to another. It ensures that a video file is compatible with the video player and/or platform it is using. Without transcoding, users would not be able to watch the video file at all.

## Slide 28: Theoretical Foundations Image Filtering
After detect the face, it is now possible to apply filters like this figure.
Scaling the image having in touch the face size and put the image in front of the face.

## Slide 29: Theoretical Foundations GIF Generation
The main features of GIF are:
  Up to 256 colors using 1 to 8 bits per pixel: allowing a single image to reference its own palette chosen from the 24-bit color space. These palette limitations make GIF less suitable for reproducing color photographs, but well-suited for simpler images such as graphics or logos with solid areas of color.
  Multiple images per file: supporting animation.
GIF images are compressed using the Lempel–Ziv–Welch (LZW) lossless data compression technique to reduce the file size without degrading the visual quality. It stores multi-byte integers with the Least Significant Bit (LSB) first (little–endian) [76].

## Slide 30: Theoretical Foundations Social Media Sharing APIs
These platforms provide a set of functionalities to external agents interact with them in a programmatic way, enabling automation of tasks like content sharing, scheduling, search, etc. These functionalities are exposed by APIs, providing a custom and well-defined interface that can be explored by developers to build custom applications that leverages on them.
Twitter API: To interact with the Twitter platform, one can make a request and retrieve its response by following these steps [87]:
  Select the end-point;
  Select a tool to make the request;
  Review the response;
  Adjust the request using parameters.

## Slide 31: Theoretical Foundations UI Framework
QT was the chosen one for the following reasons:
  Allows cross development;
  Cost: this framework is cost-friendly, not only because it has a free license, but also because its software development takes less time to develop due to the integrated environment assisting the developer.
  Implementation: it is implemented in C++, which means that it is possible to use many libraries. The wide choice of modules allow the project to have rich functionality and as a result, the software will have a Graphical User Interface (GUI) similar to a native one.

## Slide 32: Theoretical Foundations File Transfer Protocols
HTTPS:
  The communications between subsystems are made through TCP/IP, this is also used in this protocol which is an advantage;
  The data is transferred only with authentications (request and responses) which makes it more secure;
  All communication is encrypted, which makes it even more secure.
Third Party API:
  Transfer.sh: This application has easy-to-use commands in order to transfer files with a URL, there is unlimited upload, it can encrypt files and it is also possible to limit the amount of downloads and days available of downloading [104].
  Using the library curlpp with the transfer.sh API, it is possible to create a program to transfer files between nodes automatically when requested from the user

## Slide 33
3. Design

## Slide 34
3.1. Hardware

## Slide 35: Design Hardware Architecture

## Slide 36: Design Hardware Architecture
Main Controller:
  Processor: Broadcom BCM2711 processor, quad-core Cortex-A72 (ARM v8) 64-bit with 1.5GHz;
  Memory: 4GB LPDDR4 with on-die ECC;
  Connectivity: 2.4 GHz and 5.0 GHz IEEE 802.11b/g/n/ac wireless LAN, Bluetooth 5.0 with low energy, one Gigabit Ethernet port, four USB ports in which two are 3.0 and another two are 2.0;
  GPIO: standard 40-pin GPIO fully backwards-compatible with previous boards;
  Video and Sound: two HDMI ports that support up to 4kp60, a 2-lane MIPI DSI display port, a 2-lane MIPI CSI camera port and a 4-pole stereo audio and composite video port;
  Multimedia: H.265 (4Kp60 decode), H.264(1080p60 decode and 1080p30 encode) and OpenGL ES 3.0 graphics;
  SD card support: Micro SD card slot for loading operating system and data storage;
  Input power: 5V Direct Current (DC) via USB-C connector (minimum 3A), 5V DC via GPIO header (minimum 3A) and Power over Ethernet (PoE) - enabled (requires separate PoE HAT);
  Environment: it has a range of operation between 0ºC and 50ºC.

## Slide 37: Design Hardware Architecture
Motion Detection(HC-SR04):
  Operating Voltage: 5V DC;
  Operating Current: 15 milliampere (mA);
  Operating Frequency: 40 KHz;
  Maximum Range: 4 meters;
  Minimum Range: 2 centimeters;
  Ranging Accuracy: 3 millimeters;
  Measuring Angle: 15 degrees;
  Trigger Input Signal: 10 microseconds TTL pulse;
  Dimension: 45 x 20 x 15 millimeters.

## Slide 38: Design Hardware Architecture
Fragrance diffusion actuator:
  Operating Voltage: 5V DC;
  Operating Current: 300 milliampere (mA);
  Operating Power: 2 W;
  Operating Frequency: 108 kHz;
  Dimension: 35 x 20 x 17 millimeters.

## Slide 39: Design Hardware Architecture
Camera (Raspberry Pi Camera Module V2):
  Sensor: Sony IMX219 8-megapixel;
  Quality: 1080p30, 720p60;
  Interface: CSI;

## Slide 40: Design Hardware Architecture
LCD Display:

## Slide 41: Design Hardware Architecture
Speakers (Raspberry Pi Camera Module V2):
  Impedance: 8 Ohm;
  Power: 5 W;
  Interface: JST PH2.0.

## Slide 42: Design Hardware Architecture
Power Supply:
  Output: 4 USB-A 2.4 A ports.

## Slide 43: Design Hardware Architecture
Total cost:

## Slide 44: Design Hardware Interfaces Definition

## Slide 45: Design Hardware Interfaces Definition

## Slide 46: Design PCB Design
Schematic

## Slide 47: Design PCB Design
Layout

## Slide 48: Design Hardware Test Cases

## Slide 49
3.2. Software

## Slide 50: Design Component Diagram
Remote Client

## Slide 51: Design Component Diagram
Remote Server

## Slide 52: Design Component Diagram
Remote Server

## Slide 53: Design Component Diagram
Remote Server

## Slide 54: Design Component Diagram
Local System

## Slide 55: Design Component Diagram
Local System

## Slide 56: Design Component Diagram
Local System

## Slide 57: Design Component Diagram
Local System

## Slide 58: Design Deployment Diagram

## Slide 59: Design Class Diagram
Remote Client

## Slide 60: Design Class Diagram
Remote Client

## Slide 61: Design Class Diagram
Remote Client

## Slide 62: Design Class Diagram
Remote Client

## Slide 63: Design Class Diagram
Remote Client

## Slide 64: Design Class Diagram
Remote Server

## Slide 65: Design Class Diagram
Remote Server

## Slide 66: Design Class Diagram
Remote Server

## Slide 67: Design Class Diagram
Remote Server

## Slide 68: Design Class Diagram
Remote Server

## Slide 69: Design Class Diagram
Local System (1)

## Slide 70: Design Class Diagram
Local System (1)

## Slide 71: Design Class Diagram
Local System (1)

## Slide 72: Design Class Diagram
Local System (1)

## Slide 73: Design Class Diagram
Local System (2)

## Slide 74: Design Class Diagram
Local System (2)

## Slide 75: Design Class Diagram
Local System (2)

## Slide 76: Design GUI Layouts
Remote Client

## Slide 77: Design GUI Layouts
Remote Client

## Slide 78: Design GUI Layouts
Remote Client

## Slide 79: Design GUI Layouts
Remote Server

## Slide 80: Design GUI Layouts
Local System

## Slide 81: Design GUI Layouts
Local System

## Slide 82: Design GUI Layouts
Local System

## Slide 83: Design Software Test Cases
Remote Client

## Slide 84: Design Software Test Cases
Remote Server

## Slide 85: Design Software Test Cases
Local System

## Slide 86
Thank you!!
Any questions?